## Slide 1: Rubik’s Cube solving machine
Colin Roskos
Winsten Coellins

## Slide 2: Contents
Mechanic Review
  Schematic
  Lessons Learned
  Future Implementation
Code Review:
  Rubik’s Cube Representation (CLF)
  Motor Driver Representation (CLF)
  Solver (CLF)
Video of Operation
Lessons Learned
  Problems Overcome
  Problems Still to Overcome
Future Implementations/Features
Questions
CLF:
  Code Review
  Lessons Learned
  Future Implementations

## Slide 3: Mechanic Review

## Slide 4: Mechanim/schematic
New adaptor and Chasis
- Modified to fix issues with original design.
To Motor
Motor | In1 | In2 | In3 | In4
M0 – W | 3 | 5 | 7 | 11
M1 – R | 13 | 15 | 19 | 21
M2 – B | 23 | 29 | 31 | 33
M3 – G | 8 | 10 | 12 | 16
M4 – O | 18 | 22 | 24 | 26
M5 – Y | 32 | 36 | 38 | 40

## Slide 5: Lessons Learned
Test mechanical portion as you go.
  Original chassis idea would not work
Remember the cube edges rotate.
  This led to the adaptors I made to be too short.

## Slide 6: Future
Larger and Faster Stepper Motors
  I don’t need as fine of steps as the current motor gives me. A 1.8° per step would work just fine.
A metallic chasis in stead of a wooden one
  This will give more precision and adjustability to the frame.
A longer, better made adapter, with set screw.
  Using a press or solder fit did not work well in this implementation.
  A proper slip fit and set screw would have worked best.

## Slide 7: Code review

## Slide 8: Rubik’s cube representation
Code Review
Cube Object
  An Object made up of six Face Objects
  rotate, set_cell, get_cell, and cube_print functions public
Face Object
  No public functions
  Made up of a Face color and eight cells
Cell is represented as an integer.
* Show code RubicksCube.py
Lessons Learned
Using simplified representations is better than more complicated representations.
Future
A better print function; The current implementation can be a little confusing.

## Slide 9: motor representation
Code Review
A step series in List() to represent stepper signal order.
Attaches to Raspberry Pi directly
User should only use quarter_turn(), but all class functions are available.
* Show code PIMotors.py
Lessons Learned
Check the step order required by the motor, Some have half-step (the ones I used) some have full-step.
Check the fastest update limit for motors in stead of finding these experimentally.
Future
Add ability for in position to check if motor is where it is expected to be.

## Slide 11: Solver
Top Cross
Top Corners
Second Row
Bottom Cross
Complete

## Slide 12: Top cross
Code Review
* Solver.py
Lessons Learned
Modifying a general code for working with any of the four primary orientations.
Future
None for side

## Slide 13: Top Corner
Code Review
Corner in position – if not oriented correctly, remove from position
From bottom to corner - three implementations.
* Solver.py
Lessons Learned
Making sure to consider every orientation and how the solutions to other orientations occurs before coding is beneficial and can reduce code time.
Future
None for side

## Slide 14: Second row
Code Review
Only 2 locations with 2 orientations plus the rotation of the cube.
Few variations
Bottom – Left or right orientation
Side – In position or backwards
* Solver.py
Lessons Learned
This was a good starting point, but with the bottom being completed first, this was an easier task.
Future
None for side

## Slide 15: bottom cross
Code Review
Create a cross
Position edges in correct location
* Solver.py
Lessons Learned
Interpreting orientation is a big deal.
‘L’ direction specifically
Future
None for side

## Slide 16: Finish cube
Code Review
Selection of starting corner
Mechanism for switching corners
Orienting the corners
* Solver.py
Lessons Learned
Keeping orientation of a cube that is upside-down is difficult, use a physical representation with orientation.
Future
None for side

## Slide 17: Solver as a whole
Lessons Learned
Keeping organization of side structure is important.
  Having a physical model representation is valuable.
Documentation on orientation of the cube needs to be very clear to be helpful.
Future Implementation
Short-cut algorithms
  No cube is more than 20 moves from solution.

## Slide 18: Operation

## Slide 19: Lessons Learned
Problems Overcome
Finding a way to visualize and remember orientation reliably.
Still to Overcome
Reducing steps further.
Stepper motor consistency.
Fix wiring and other physical implementation issues.

## Slide 20: Future implementations
Better, faster, stepper motors.
Better prototype board.
Improved power source.
Improved solution algorithm
Improved chassis and adapter designs

## Slide 21
?

## Slide 22: Sources
https://ruwix.com/the-rubiks-cube/how-to-solve-the-rubiks-cube-beginners-method/
RPi.GPIO Library: https://pypi.org/project/RPi.GPIO/
Rubik’s Cube Image: https://www.rubiks.com/media/catalog/product/cache/9c57e2fe71f8a58f6afba681a0a15dd4/r/u/rubik-3x3-solved.jpg